Khari Ollivierre
Lab 3
Section 1490

# Pseudocode
### Lab 3a
Define clock control/status and IOREG codes as constants
Define CLKEVOUT code for PORTC_6 output ("00000001")

BEGIN MAIN
CALL CLKSEL
SET PORTC_7 to output
SET PORTCFG_CLKEVOUT to constant defined above
WHILE true
END WHILE
END MAIN

BEGIN CLKSEL
SET CPU_CCP to IOREG (0xD8)
WHILE OSC_STATUS is ~(status constant for desired clock)
END WHILE
SET OSC_CTRL to (control constant for desired clock)
SET CLK_PSCTRL to (chosen prescalar settings)
SET CLK_CTRL to (control constant for desired clock)
END CLKSEL

### Lab 3b
Define clock control/status and IOREG codes as constants
DEFINE PERIOD_L as constant "0x00"
DEFINE PERIOD_H as constant "0xFF"
DEFINE C0_CTRL as constant "0x07"

BEGIN MAIN
LOAD 4 registers used in CLKSEL with codes for 2 MHz clock
CALL CLKSEL
CALL CNTCFG_C0
SET PORTC to output
WHILE true
OUTPUT TCCO_CNTL to PORTC
END WHILE
END MAIN

BEGIN CLKSEL
SET CPU_CCP to IOREG (0xD8)
WHILE OSC_STATUS is ~(status constant for desired clock)
END WHILE
SET OSC_CTRL to (control constant for desired clock)
SET CLK_PSCTRL to (chosen prescalar settings)
SET CLK_CTRL to (control constant for desired clock)
END CLKSEL

BEGIN CNTCFG_C0
LOAD PERIOD_L into TCC0_PERL
LOAD PERIOD_H into TCC0_PERH
LOAD C0_CTRL into TCC0_CTRLA
END CNTCFG_C0
DEFINE EBI_CTRL constant "0x41"
DEFINE EBI_CS0_CTRLA constant "0x42"
DEFINE EBI_CS0_CTRLB constant "0x06"
DEFINE EBI_CS0_BASEADDR constant "0x2000"
DEFINE TDATA constant "0xA5"
DEFINE TDATA_ADDR constant "0x04"

DEFINE PORTH pins as appropriate control signals

BEGIN MAIN
CALL EBICONFIG
SET CS0 to 0

// Load value for writing
LOAD TDATA into R18
WHILE true
LOAD TDATA_ADDR into Z // Load high and low bytes individually
CALL WRITE
LOAD TDATA_ADDR into Z
CALL READ	// Read operation results stored in R16
END WHILE
END MAIN

BEGIN MEMADDRLD
SET PORTK to ZL
INC Z
END MEMADDRLD

BEGIN WRITE
CALL MEMADDRLD
SET PORTJ to R18	// Low byte to be written
LSR R18	// Mask out low byte
CALL WRTGL
CALL MEMADDRLD
SET J[3-0] to R18	// High byte to be written
CALL WRTGL
END WRITE

BEGIN WRTGL
SET CS to 0
SET ALE to 1
SET WE to 0
// Just in case
NOP
NOP
NOP
NOP
NOP
SET CS to 1
SET ALE to 0
SET WE to 0
END WRTGL

BEGIN READ
CALL MEMADDRLD
CALL RDTGL
LOAD PORTJ into R16	// Low byte read
CALL MEMADDRLD
CALL RDTGL
LOAD PORTJ into R17	// High byte read
LSL R17	// Shifted to its correct position
ADD R16, R17	// Concatenate both bits
CLR R17
END READ

BEGIN RDTGL
SET CS to 0
SET ALE to 0
SET RE to 1
NOP
NOP
NOP
NOP
SET CS to 1
SET ALE to 0
SET RE to 0
END RDTGL

BEGIN EBICONFIG
SET EBI_CTRL to constant defined above
SET EBI_CS0_CTRLA to constant defined above
SET EBI_CS0_BASEADDR to constant defined above
SET PORTH to output for control signals
SET PORTK to output for address signal

// Control signals predefined above
SET CS to 1
SET WE to 1
SET RE to 1
SET ALE to 0
SET CS3 to 1
SET CS2 to 1
SET CS1 to 1
SET CS0 to 1
END EBICONFIG

### Lab 3d
// Reserved registers: R16 (Read register), R17 (temp register for reads), R18 (write register)

Define clock control/status and IOREG codes fo 32 MHz clock as constants
Define CLKEVOUT code for PORTC_6 output ("00000001")

DEFINE EBI_CTRL constant "0x41"
DEFINE EBI_CS0_CTRLA constant "0x42"
DEFINE EBI_CS0_CTRLB constant "0x06"
DEFINE EBI_CS0_BASEADDR constant "0x3000"
DEFINE PORTH pins as EBI control signals

DEFINE PERIOD_L as constant "0xA2"
DEFINE PERIOD_H as constant "0x07"
DEFINE C0_CTRL as constant "0x07"
DEFINE CCAFLAGS as "10000000"

BEGIN MAIN
SET PORTA as input for switches
SET PORTC as output for LEDs
CLR Z	// For accessing external memory
CALL CLKSEL
CALL EBICONFIG
CALL CNTCFG_C0
CLR R19	// Register for counter flags

WHILE true
WHILE R19 != CCAFLAGS
LOAD TCC0_INTFLAGS into R19
R19 << 3	// Mask out extra flag bits
END WHILE
LOAD PORTA into R18
CALL WRITE	// Write switch data to memory
CLR Z	// Reset Z to original memory location
CALL READ	// Read memory into R16
STORE R18 on PORTC	// Output read data to LEDS
END WHILE
END MAIN

BEGIN CLKSEL
SET CPU_CCP to IOREG (0xD8)
WHILE OSC_STATUS is ~(status constant for desired clock)
END WHILE
SET OSC_CTRL to (control constant for desired clock)
SET CLK_PSCTRL to (chosen prescalar settings)
SET CLK_CTRL to (control constant for desired clock)
END CLKSEL

BEGIN CNTCFG_C0
LOAD PERIOD_L into TCC0_PERL
LOAD PERIOD_L into TCC0_CCAL
LOAD PERIOD_H into TCC0_PERH
LOAD PERIOD_H into TCC0_CCAH
LOAD C0_CTRL into TCC0_CTRLA
END CNTCFG_C0

BEGIN MEMADDRLD
SET PORTK to ZL
INC Z
END MEMADDRLD

BEGIN WRITE
CALL MEMADDRLD
SET PORTJ to R18	// Low byte to be written
LSR R18	// Mask out low byte
CALL WRTGL
CALL MEMADDRLD
SET J[3-0] to R18	// High byte to be written
CALL WRTGL
END WRITE

BEGIN WRTGL
SET CS to 0
SET ALE to 1
SET WE to 0
// Just in case
NOP
NOP
NOP
NOP
NOP
SET CS to 1
SET ALE to 0
SET WE to 0
END WRTGL

BEGIN READ
CALL MEMADDRLD
CALL RDTGL
LOAD PORTJ into R16	// Low byte read
CALL MEMADDRLD
CALL RDTGL
LOAD PORTJ into R17	// High byte read
LSL R17	// Shifted to its correct position
ADD R16, R17	// Concatenate both bits
CLR R17
END READ

BEGIN RDTGL
SET CS to 0
SET ALE to 0
SET RE to 1
NOP
NOP
NOP
NOP
SET CS to 1
SET ALE to 0
SET RE to 0
END RDTGL

BEGIN EBICONFIG
SET EBI_CTRL to constant defined above
SET EBI_CS0_CTRLA to constant defined above
SET EBI_CS0_BASEADDR to constant defined above
SET PORTH to output for control signals
SET PORTK to output for address signal

// Control signals predefined above
SET CS to 1
SET WE to 1
SET RE to 1
SET ALE to 0
SET CS3 to 1
SET CS2 to 1
SET CS1 to 1
SET CS0 to 1
END EBICONFIG

### Lab 3c